Draft DMRGateway Install notes
DMRGateway is a collection of software and hardware modules to connect AllStarLink to a DMR network via IPSC. DRMGateway (DMRG) can connect to a c-Bridge based network (DMR-MARC, DCI) or a BrandMeister Network. The basic configuration of DMRG is contained in the document DMRGatewayDiagram.pdf. DMRG uses software and hardware from DVSwitch (DVS), DMRlink(DMRl), NWDigital (NWD) and AllStarLink (ASL). Each module is configured and operates separately. UDP data is used for communication between modules. This does allow the modules to be spread across multiple hosts. That type of configuration is outside the scope of this document. We will configure each module and verify proper operation of each module before moving on to the next. Once all modules are operating, we will verify proper operation of the complete system. A raspberry Pi is sufficient to run the system. That is not to say it only runs on a Pi, The Pi is just a example for this install document. Everything will be done as root. login to the Pi as root or execute a sudo -s if the login you use has sudo privileges.  This is MUCH easier then sudo this, sudo that... If you are not comfortable operating in a Linux environment, stop now. This is not for you. We will be using Raspbian, a Debian derivative. All the scripts and downloaded programs are in the /srv directory. Some will be copied to other directories during installation.
I will start with the hardware. For this document we are going to use a Raspberry Pi2 (Pi) and a DV3000u (DV) from NWD. The DV is a Vocoder. It's job is to take AMBE data and convert it to analog (PCM) and PCM to AMBE. The DV we will use is a USB device. It simply plugs into a USB port on the Pi. Communications from the Pi to the DV is serial. Our first task is to connect the DV to the Pi and ensure proper communications. I will use Python scripts from NWD to test communications to and from the DV.
Install and test the DV3000
1: Make sure your installation is up to date. Execute apt-get update
2: Execute apt-get upgrade -y
3: I usually reboot after a upgrade, just habit on a new system. Execute reboot
4: Plug the DV into a USB port on the Pi.
5: Verify the DV has been recognized by the Pi. You should have a device in /dev. The device is ttyUSBx. You can verify this by executing ls /dev/ttyUSB* before and after plugging in the DV. If you already have something else using ttyUSB0, the DV will become ttyUSB1.
 6: We now need the python test scripts from NWD. I have copied the test script AMBEtest3.py from <https://github.com/dl5di/OpenDV/tree/master/DummyRepeater/DV3000> to the DMRG repository.
 7: Checkout DMRGateway from github. Execute cd /srv Then execute git clone https://github.com/N4IRS/DMRGateway.git
 8: The python test script needs one additional python module to run. Execute apt-get install python-serial to install the python-serial module.
 9: Go to the /srv/DMRGateway/DV3000 directory. Execute cd  /srv/DMRGateway/DV3000 . Executing a ls will show you the test script, AMBEtest3.py.
10: Execute python AMBEtest3.py -n -s /dev/ttyUSB0

Your output should look like this. Important data is in bold.
=====================================================================
# python AMBEtest3.py -n -s /dev/ttyUSB0
Setting ...
/dev/ttyUSB0
d
8
N
1
False
False
False
Reset
6100010033
Wrote: 5 bytes
a9
Product ID
6100010030
Wrote: 5 bytes
a
 0AMBE3000R
Version
6100010031
Wrote: 5 bytes
a11V120.E100.XXXX.C106.G514.R009.B0010411.C0020208
Set DSTAR Mode
61000c000a013007634000000000000048
Wrote: 17 bytes
a
=====================================================================
If you do not receive the data in bold, STOP !!! Without communications to and from the DV, you can go no further. Leave the DV connected, we will need it for the next module.
This concludes testing communications with the DV.

Install and test DMRGateway
DMRG receives AMBE data from ambe_audio, formats the AMBE and sends it to the DV. The DV "converts" the AMBE to PCM and returns it to DMRG. The PCM is then sent to ASL. The same is true in the other direction.

  1: DMRG is a program specific to the platform (processor) you are running. We are running a RPi2 so we need the the armv7 version of DMRG.
  2: Execute cd /srv/DMRGateway
  3: Create the destination directory by executing mkdir -p /opt/DMRGateway
  4: Copy the proper version of DMRG to the destination directory. Execute cp DMRGateway.armv7 /opt/DMRGateway/ DMRGateway
  5: Copy the DMRG configuration file to the destination directory. Execute cp DMRGateway.ini /opt/DMRGateway
  6: Change directory to the DMRG directory. Execute cd /opt/DMRGateway
  7: Execute ls to see the 2 files are in the DMRG directory
  8: DO NOT edit DMRGateway.ini UNLESS your DV is not at /dev/ttyUSB0
  9: Run DMRG in the foreground by executing ./DMRGateway DMRGateway.ini
Your output should look like this. Important data is in bold.
=====================================================================

# ./DMRGateway DMRGateway.ini
DMRLink Gateway
Setting [GENERAL] outputAudioDevice -> /dev/null
Setting [GENERAL] inputAudioDevice -> /dev/null
Setting [GENERAL] decoderFallBack -> false
Setting [GENERAL] useMicrophone -> false
Setting [GENERAL] useVox -> true
Setting [GENERAL] voxDecay -> 2
Setting [GENERAL] voxTrigger -> 200
Setting [AMBE_AUDIO] server -> 127.0.0.1
Setting [AMBE_AUDIO] fromDMRPort -> 31000
Setting [AMBE_AUDIO] toDMRPort -> 31003
Setting [USRP] server -> 127.0.0.1
Setting [USRP] toASLPort -> 32001
Setting [USRP] fromASLPort -> 34001
Setting [USRP] aslAudio -> AUDIO_USE_AGC
Setting [USRP] agcGain -> -20
Setting [USRP] dmrAudio -> AUDIO_USE_BPF
Setting [USRP] dmrGain -> 0.35
Setting [DV3000] server -> /dev/ttyUSB0
Setting [DV3000] port -> 460800
Setting [DV3000] serial -> true
ioctl reset error    <----------------------------------------- Ignore this
ioctl speed error   <----------------------------------------- Ignore this
ioctl stereo error  <----------------------------------------- Ignore this
ioctl setfmt error  <----------------------------------------- Ignore this
Audio In/Out Device: /dev/null
Open UDP listener on 127.0.0.1:31000
Open USRP on 127.0.0.1:32001
Begin DV3000 decode
Using hardware AMBE decoder
Starting DMRLink --> USRP thread
Open UDP listener on 127.0.0.1:34001
Starting USRP --> DMRLink thread
Press Control C to exit dmrlink.py
=====================================================================
If you do not receive the data in bold, STOP !!!  DMRGateway is not communicating with the DV, you can go no further.
These lines tell you how DMRG is communicating with the DV.
Setting [DV3000] server -> /dev/ttyUSB0 <--- USB Device name
Setting [DV3000] port -> 460800 <--- baud rate
Setting [DV3000] serial -> true <--- We are communicating serial
This concludes testing DMRG.

Install and test DMRlink / ambe_audio
The two python programs, dmrlink.py and ambe_audio.py are used to communicate with the IPSC network. In simple terms, dmrlink.py connects to the master and passes AMBE data to ambe_audio.py (Don't shoot me Cort!)
You need both programs, but they can be tested separately. This makes troubleshooting much easier.
   1: Checkout DMRlink from github. Execute cd /srv Then execute git clone https://github.com/n0mjs710/DMRlink.git
   2: Execute cd /srv/DMRlink
   3: DMRL includes a install script that will install required Python modules, create the destination directory in /opt and copy the needed files.
   4: Execute cd /srv/DMRlink
   5: Execute ./mk-dmrlink
   6: DMRl is now installed in /opt/dmrlink
   7: Change to the /opt/dmrlink/ambe_audio directory. Execute cd /opt/dmrlink/ambe_audio
   8: We need a configuration file for dmrlink.py Execute cp dmrlink_SAMPLE.cfg dmrlink.cfg
   9: For testing purposes, we want to log output to go to the console (screen)
 10: Edit the following lines in dmrlink.cfg
 11: Line 62 in the LOGGER section Change LOG_HANDLERS: file to LOG_HANDLERS: console
 12: Line 75 in the ALIASES section Change PATH: ./ to PATH: ../
 13: Save your work
 14 Execute python dmrlink.py
Your output should look like this.
=====================================================================

# python dmrlink.py
INFO DMRlink 'dmrlink.py' (c) 2013 - 2015 N0MJS & the K0USY Group - SYSTEM STARTING...
INFO (SAMPLE_PEER) IPSC Instance Created: 12345, 0.0.0.0:50000
INFO (SAMPLE_PEER) Registering with the Master: 1.2.3.4:50000
This line will keep repeating. This is normal at this point of the install.
INFO (SAMPLE_PEER) Registering with the Master: 1.2.3.4:50000
Press Control C to exit dmrlink.py
=====================================================================
If you do not receive the output above, STOP !!! Something is wrong with the dmrlink install, or the configuration file is damaged.

We will now add valid configuration data to dmrlink.cfg so we can test further we are going to connect to BrandMeister for this part of the test.
 15: Edit the following lines in dmrlink.cfg
 16: Line 147 in the SAMPLE_PEER section Change AUTH_ENABLED: True to AUTH_ENABLED: False
 17  Line 149 in the SAMPLE_PEER section Change MASTER_IP: 1.2.3.4 to MASTER_IP: 64.94.238.196
 18  Line 150 in the SAMPLE_PEER section Change MASTER_PORT: 50000 to MASTER_PORT: 55001
 19: Save your work
 20 Execute python dmrlink.py
Your output should look like this. Important data is in bold.
=====================================================================

# python dmrlink.py
INFO DMRlink 'dmrlink.py' (c) 2013 - 2015 N0MJS & the K0USY Group - SYSTEM STARTING...
INFO (SAMPLE_PEER) IPSC Instance Created: 12345, 0.0.0.0:50000
INFO (SAMPLE_PEER) Registering with the Master: 64.94.238.196:55001
WARNING (SAMPLE_PEER) Registration response (we requested reg) from the Master: 3108, 64.94.238.196:55001 (1 peers)
INFO (SAMPLE_PEER), No Peer List - Requesting One From the Master
=====================================================================
If you do not receive the output above, STOP !!! Something is wrong with the dmrlink install, or the configuration file is damaged.

Now we will do initial testing of ambe_audio.py For the first part of the test, we will not edit the configuration file.
 1: Execute python ambe_audio.py
Your output should look like this. Important data is in bold.
=====================================================================

# python ambe_audio.py
INFO DMRlink 'ambe_audio.py' (c) 2015 N0MJS & the K0USY Group - SYSTEM STARTING...
INFO ID ALIAS MAPPER: 'peer_ids.csv' is current, not downloaded
INFO ID ALIAS MAPPER: 'subscriber_ids.csv' is current, not downloaded
INFO ID ALIAS MAPPER: peer_ids dictionary is available
INFO ID ALIAS MAPPER: subscriber_ids dictionary is available
INFO ID ALIAS MAPPER: talkgroup_ids dictionary is available
INFO (SAMPLE_PEER) IPSC Instance Created: 12345, 0.0.0.0:50000
INFO section = SAMPLE_PEER
ERROR Section SAMPLE_PEER was not found, using DEFAULTS
INFO debug = False
INFO outToFile = False
INFO outToUDP = True
INFO gateway = 127.0.0.1
INFO toGatewayPort = 31000
INFO remoteControlPort = 31002
INFO fromGatewayPort = 31003
INFO gatewayDmrId = 0
INFO tgFilter = 9
INFO txTg = 9
INFO txTs = 2
INFO DMRLink ambe server
Error: gatewayDmrId must be set (greater than zero)
=====================================================================
If you do not receive the output above, STOP !!! Something is wrong with the ambe_audio install, or the configuration file is damaged.